###### Technical specifications

924 models 78-85

925 turbo models79-84

924 Carrera GT models 81

Contents

Page General

Important conversion factors and new dimensioning units..................3

Survey of type designations .............................................3

Engine number codes .....................................................3

Chassis number codes models 78...79......................................3

Chassis number codes model 80 ...........................................3

Chassis number codes from model 81.......................................4

Manual and automatic transmissions 924/924 turbo ........................4

Transmission number codes 924............................................4

Transmission number codes 924 turbo .....................................4

Engine

Engine data..............................................................5

Technical data 924 engine type XK/XJ ....................................5

Technical data 924 CarreraGT. ...........................................6

Torque specifications - engine 924/924 turbo ............................6

Tolerances and wear limits ..............................................7

Repair stages tor crankshaft ............................................7

Checking pistons and cylinder bores 924 .................................8

Checking pistons and cylinder bores 924 turbo ...........................8

Checking valve dimensions and valve guides ..............................8

Adjusting screw notching ................................................8

Checking and adjusting valve play, reworking intake valve ...............8

Reworking valve seats ...................................................8

Tightening specifications-cylinder head bolts 924 .......................8

Machining the cylinder head mating face .................................8

Main testing and adjusting values for engine ............................9

Measuring boost pressure 924 turbo ......................................9

V-belt dimensions and coolant mixing table ..............................9

Page Transmission and clutch

Torque specifications for manualtransmission,

central tube, clutch and actuating elements 924 ........................9

Technical data - clutch .................................................10

Technical data - 4-speed manual transmission 924 ........................11

Technical data - 5-speed manual transmission 924 ........................11

Torque specifications -automatic transmission 924 .......................11

Torque specifications - autom. transmission actuating elements 924 ......11

Torque specifications - accelerator actuation (automatic) 924 ...........11

Torque specifications-central tube (automatic) 924 ......................12

Technical data-automatic transmission 924 ...............................12

Pressure-testing hydraulic control unit .................................12

Torque specifications - manual transmission 924 turbo ...................13

Torque specifications - clutch, central tube,

transmission suspension, shift actuation 924 turbo ......................13

Torque specifications -manual transmission type 016G 924 turbo ..........13

Torque specifications - Clutch, central tube, transmission

suspension and shift actuation type 016G 924 turbo ......................13

Technical data - 5-speed manual transmission 924 turbo ..................13

Front axle, steering, rear axle and wheels

Torque specifications -front axle 924/924 turbo .........................14

Torque specifications -steering 924/924 turbo ...........................14

Torque specifications -rear axle 924/924 turbo ..........................14

Technical data-front axle 924 ...........................................14

Technical data-front axle 924 turbo .....................................14

Technical data-steering 924 .............................................14

Technical data-steering 924turbo ........................................14

Technical data - rear Axle 924...........................................14

Technical data - rear axle 924 turbo ....................................14

Checking disk wheels ....................................................15

Tires, wheels, tire pressures ...........................................15

Wheel alignment adjustment values 924/924 turbo .........................15

Page Brake system

Torque specifications-mech. brake system ................................15

Torque specifications - hydr. brake system ..............................15

Technical data - brake system 924........................................15

Technical data -brake system 924 turbo/CarreraGT ........................15,16

Air conditioning

Technical data - air conditioning as from Model 79 ......................17

Torque specifications - air conditioning ................................17

### Electrical system

Relays ..................................................................17

Fuses ...................................................................17

General technical data

Performance figures .....................................................18

Dimensions ..............................................................18

Weights .................................................................18

Filling capacities.......................................................18

Important Conversion Factors and New Dimensioning Units

Former units 	Present units
Pressure Technical atmosphere 	at(kp/cm2) Bar (bar)
Output Horsepower 	HP Kilowatt (kW)
Force Kilopond 	kp Newton (N)
Torque Kilopondmeter 	kpm Newtonmeter(Nm) '

Conversion factors

at(kp/cm2) in bar 	x 0.981
kp in N 	x 9.81
HP in kW 	x 0.736
kpm in Nm (ftlb) 	x 9.81
m/s in km/h 	x 3.6
at in mmHG 	x 735.56
km/h in mph (miles) 	x 0.621
(F (Fahrenheit) in(C 	(°F-32)x 0.555
I in U.S. gal 	x 0.264
I in Imp. gal 	x 0.22

To convert tightening torques from kpm into Nm, the conversion factor 10 can be used. This is sufficient for workshop applications.

### Survey of Type Designations

| Model year designation | Vehicle type designation | Engine type designation | Displa-cem-ent act. Cm3 | DIN-kW (HP) | Stroke/ Bore (mm) | Compression ratio | Fuel-induction system | Engine numbers | Chassis numbers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1978-1979 | 924 Europe, RoW 924 USA, Japan, Calif. | XK/XJ XG/XE | 1984 1984 | 92/125 85/115 | 84.4/86.5 84.4/86.5 | 9.3:1 8.5:1 | K-Jetronic K-Jetronic K-Jetronic | XK 000001 onwards XG 000001 onwards XG 000001 onwards | 9248100001-99999 924 82 00001-99999 924 83 00001-99999 (Japan) |
| 1980 | 924 Europe, RoW 924 USA, Canada, Japan | XK/XJ VC | 1984 1984 | 92/125 85/115 | 84.4/86.5 84.4/86.5 | 9.3:1 9.0:1 | K-Jetronic K-Jetronic | XK 000001 onwards VC 000001 onwards | 92 АО 410001-9999 92 АО 43 0001-9999 |
| 1981-1982 | 924 Europe, RoW 924 USA, Canada, Japan | XK/XJ VC | 1984 1984 | 92/125 85/115 | 84.4/86.5 84.4/86.5 | 9.3:1 9.0:1 | K-Jetronic K-Jetronic | XK 000001 onwards VC 000001 onwards | WPO ZZZ 92 Z BN 40 0001-9999 WPO AAO 92 0 BN 45 0001 -9999 |
| 1983-1985 | 924 Europe, RoW | XK/XJ | 1984 | 92/125 | 84.4/86.5 | 9.3:1 | K-Jetronic | XK 000001 onwards | WPO ZZZ 92 Z DN 40 0001 -9999 |
| 1979-1980 | 924 turbo, Europe,RoW 924 turbo, USA, Canada Japan | M31/01 M31/02 | 1984 1984 | 125/170 110/150 | 84.4/86.. 84.4/86. | 5 7.5:1 5 7.5:1 | K-Jetronic K-Jetronic | 31010001-9999 31020001-9999 | 93 АО 14 0001-9999 93 А015 0001-9999 |
| 1981-1982 | 924 turbo, Europe, RoW 924 turbo, USA, Canada Japan | M31/03 M31/04 | 1984 1984 | 130/177 115/156 | 84.4/86. 84.4/86. | 5 8.5:1 5 8.0:1 | K-Jetronic K-Jetronic | 31030001-9999 31040001-9999 | WPO ZZZ 93 Z BN 100001-9999 WPO AAO 93 0 CN 15 0001 -9999 |
| 1982-1984 | 924 turbo, Italy | M31/03 | 1984 | 130/177 | 84.4/86. | 5 8.5:1 | K-Jetronic | 3103 0001-9999 | WPO ZZZ 93 Z DN 10 0001 -9999 |

Engine Number Codes

| e.g. | XK | 000001 |
| --- | --- | --- |
|  | Code letters engine type | Serial no. continuous irrespective of model year, when code letters identical. With new code letters/engine type, serial no. starts again at 000001. |

| Code letters range engine type | Techn. data | Fitted in vehicle type | Engine no. Letters |
| --- | --- | --- | --- |
| XK XJ XG XE VC | 92KW/125HP 92kW/125HP 85KW/115HP 85kW/115HP 85kW/115HP | 924-Europe, Rest of World 924-Europe,Rest of World right-hand drive 924-USA, Japan 924 California 924-USA, Canada California, Japan | 000001 onwards 000001 onwards 000001 onwards 000001 onwards 000001 onwards |

Engine number codes (8-digit) 924 turbo

3 1 01 0001 -9999         Europe/Rest of World (left and

right-hand drive)

31 02 0001-9999           USA/California/Canada/Japan

31 03 0001-9999           Europe/Rest of World (left and

right-hand drive)

31 04 0001-9999            USA/California/Canada/Japan

Serial no.

Type designation

3101 = T25kW (170 HP)

3102 = 110 kW (150 HP)

3103 = 130 kW (177 HP)

3104= 115 kW (156 HP)

Chassis Number Codes, Models 78...79

1. Chassis no. codes (10-digit)

924   8         1               00001

Type Model year Model version    Serial no.

8 = 1978   1 = Europe,      00001 to 99999

9 = 1979   Rest of World

2 = USA,         Serial no.starts

California       at beginning again for

3 = Japan        each model year and country

category

Chassis Number Codes, Model Year 80

The following changes are effective from model year 1980 for the chassis no.:

1. The 1st and 2nd digits signify basic type.

2. The 3rd digit signifies model year, internationally established as A for 1980.

3. The 4th digit indicates the factory. For model year 1980 the code is 0.

4. The 5th digit, in conjunction with digits 1 and 2, provides further identification of the vehicle. The 6th digit indicates the engine version.

5. The remaining 4 digits form the serial no.

The example below makes the changes clear:

924___________________Model year 1979   924 91 00001

|_________Model year 1980   92 A041 0001

924 turbo_____________Model year 1979   9249400001

|_________Model year 1980   93 A014 0001

Chassis Number Codes, Model 80

Chassis number codes 924

| 92 АО 41 0001 – 9999 92 АО 42 0001 - 9999 92 АО 43 0001 - 9999 92 АО 44 0001 – 9999 | Europe / Rest of World And beyond if more than 9999 vehicles USA/California/Canada/Japan And beyond if more than 9999 vehicles |
| --- | --- |
|  | Serial no. Engine version 1 2000 cm3 92kW/125HP 2 2000 cm3,92kW/125HP 3 2000 cm3, 85kW/115HP 4 2000 cm3, 85kW/115HP Type supplement (this number designates model 924 in conjunction with first 2 digits) Place of production (Factory code initially designated as 0.) Model year A =1980 В = 1981 Type code (vehicle model) |

The 924 turbo is designated type 931 internally.

1. Chassis no. codes (10-digit)

| 93 А0 14 0001- 9999 93 А0 15 0001 –9999 | Europe/Rest of World USA/California/Canada/Japan |
| --- | --- |
|  | Serial no. Engine version 4= 2000 cm3 125 kW/170 HP 5 = 2000 cm3, 110 kW/150 HP Type supplement Place of production Model year A =1980 B = 1981 Type code |

Chassis Number Codes as from Model 81

Chassis number codes 924

| WPO ZZZ 92 Z С N 40 0001 - 9999 WPO AAO 92 О С N 45 0001 – 9999 | Europe/Rest of World USA/Canada/Japan |
| --- | --- |
| ¦ | Serial no. Code for body type and engine Indicates vehicle type together with digits 7 and 8 Place of production Model year (B = 81, С = 82, D = 83, E = 84, F = 85) Test code Vehicle type together with 12th digit Filling code or VDS code for USA and Canada versions World manufacturer code |

Chassis number codes 924 turbo

WPO ZZZ 93 Z С N 100001 - 9999 Europe/Rest of World

WPO AAO 930 С N 150001 – 9999 USA/Canada/Japan

Manual and automatic transmissions 924/924 turbo

| Model | Ident. letters | Type | Fitted in | model year |
| --- | --- | --- | --- | --- |
| 088/6 088/A 016Z 016Y 016/8 016/9 016/8 016/8 016/9 016/9 016/9 | YR XT VA VB VQ VR MD 4Q MF 5Q ME | 4-speed 4-speed 5-speed 5-speed 5-speed 5-speed 5-speed 5-speed 5-speed 5-speed 5-speed | Europe, RoW USA, Japan Europe, RoW USA Europe, RoW USA, Japan Europe, RoW Europe, RoW with lock USA USA, Japan with lock Japan | 78/79 78/79 78/79 78/79 80 80 from 81 82 from 81 82 from 81 |

For repair purposes these transmissions differ only slightly from model 80.

| 087/3 087/6 | RK RL | Automatic Automatic | Europe, RoW USA, Japan, California | from 78 from 78 |
| --- | --- | --- | --- | --- |

924 turbo

| G31/01 G31/02 016G 016G | MB MX |  | 5-speed 5-speed 5-speed 5-speed | Europe, RoW USA, Japan USA Japan | 79.. .84 up to 80 81/82 81/82 |
| --- | --- | --- | --- | --- | --- |

Transmission Number Codes 924

| Model year | Number | Transmission type | Vehicle type |
| --- | --- | --- | --- |
| 1978, 1979 1980 1981 | YR1902 8 XT XX XX 8 RK XX XX 8 RL XX XX 8 VA 00001-99999 VB 00001-99999 VQ XX XX 0 VR XX XX 0 RK XX XX 0 RL XX XX 0 MD XX XX 1 MFXXXX1 ME XX XX 1 RK XX XX 1 RLXXXX1 | 088/6 - 4-speed 088/A - 4-speed 087/3 – Automatic 087/6 - Automatic Production year 8 = 1978, 9 = 1979 Production month Production day Identifying letters 016Z - 5-speed 016Y - 5-speed Serial number 016/8-5-speed 016/9-5-speed 087/3–Automatic 087/6– Automatic 016/8-5-speed 016/9-5-speed 016/9-5-speed 087/3 – Automatic 087/6 – Automatic | 924 Europe/RoW 924 USA/Japan 924 Europe/RoW 924 USA/Japan 924 Europe/RoW 924 USA/Japan 924 Europe/RoW 924 USA/Japan 924 Europe/RoW 924 USA/Japan 924 Europe/RoW 924 USA/Canada 924 Japan 924 Europe/RoW 924 USA/Japan/Canada |
| 1982 | М019 02 2 4Q XX XX X | 016/8 - 5-speed 016/8 5-speed w. Differential lock | 924 Europe/RoW 924 Europe/RoW |
|  | MF XX XX X 5Q XX XX X | 016/9 - 5-speed 016/9 - 5-speed w. Differential lock | 924 USA/Canada 924 USA/Japan |
|  | ME XX XXX | 016/9 - 5-speed | 924 Japan |
|  | RK XX XX X RL XX XX X | 087/3 - Automatic 087/6 - Automatic | 924 Europe/RoW 924 USA/Japan/ Canada |
| 1983 | MD 19 02 3 4Q XX XX X | 016/8 - 5-speed 016/8- 5-speed w. Differential lock | 924 Europe/RoW 924 Europe/RoW |
|  | RK XX XX X | 087/3 - Automatic (up to 09.1982) | 924 Europe/RoW |
|  | RCC XX XX X | 087/3 - Automatic (from 10.1982) | 924 Europe/RoW |
| 1984, 1985 | MD19024 | 016/8 - 5-speed | 924 Europe/RoW |
|  | 4Q XX XX X | 016/8- 5-speed w. Differential lock | 924 Europe/RoW |
|  | RCC XX XXX | 087/3 - Automatic | 924 Europe/RoW |

Transmission Number Codes 924 turbo

| Model year | Number | Transmission type | Vehicle type |
| --- | --- | --- | --- |
| 1979, 1980 | 31 01 00001 (12) - 99999 3102 00001 (12)- 99999 | G31/01 - 5-speed G 31/02 - 5-speed Differential lock | 924 turbo Europe/RoW 924 turbo USA/Japan |
| 1981 | 31 01 00001 (12) -99999 016 G 000001 -99999 | G31/01 - 5-speed MB = 016G - 5-speed MX = 016G - 5-speed | 924 turbo Europe/RoW 924 turbo USA/Can. 924 turbo Japan |
| 1982 | 31 01 00001 (12) -99999 016G 00001 -99999 016G 00001 -99999 016G 00001 -99999 | G31/01 - 5-speed MB = 016G - 5-speed MX = 016G - 5-speed 6Q = 016G - 5-speed with differential lock | 924 turbo Europe/RoW 924 turbo USA/Can. 924 turbo Japan 924 turbo USA/ Canada/Japan |
| 1983 1984 | 31 01 00001 (12) -99999 31 01 00001 (12) -99999 | G31/01 - 5-speed G31/01 - 5-speed | 924 turbo Italy 924 turbo Italy |

Engine Data

| Engine type Model year |  | 924 XK 924 XJ 78…85 | 924 XG 924 XE 78…79 | 924 VC 80...82 | M31/01 turbo 79...80 | M31/02 Turbo 73...80 | M31/03 turbo 81..84 | M31/04 turbo 81.„82 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No. of cylinders |  | 4 | 4 | 4 | 4 | 4 | 4 | 4 |
| Bore | mm/in. | 86.5/3.41 | 86.5/3.41 | 86.5/3.41 | 86.5/3.41 | 86.5/3.41 | 86.5/3.41 | 86.5/3.41 |
| Stroke | mm/in. | 84.4/3.32 | 84.4/3.32 | 84.4/3.32 | 84.4/3.32 | 84.4/3.32 | 84.4/3.32 | 84.4/3.32 |
| Displacement (actual) | Cm3/in3 | 1984/121.06 | 1984/121.06 | 1984/121.06 | 1984/121.06 | 1984/121.06 | 1984/121.06 | 1984/121.06 |
| Compression ratio |  | 9.3:1 | 8.5:1 | 9.0:1 | 7.5:1 | 7.5:1 | 8.5:1 | 8.0:1 |
| Max. engine power, |  |  |  |  |  |  |  |  |
| 80/1269/EWG | kW/HP | 92/125 | 85/115 | 85/115 | 125/170 | 110/150 | 130/177 | 115/156 |
| (Net Power, SAE J1349) | kW/HP |  | 82/110 |  | 121/162 | 106/143 | 126/169 | 115/154 |
| At engine speed max. Torque, | Rpm | 5800 | 5750 | 5750 | 5500 | 5500 | 5500 | 5750 |
| 80/1269/EWG | Nm/kpm | 165/16.8 | 156/15.9 | 156/15.9 | 245/25 | 206/21 | 250/25.5 | 210/21.4 |
| (Net Torque, SAE J1349) | Nm/ftib |  | 151/111.3 |  | 237/175 | 199.4/147 | 242/184.5 | 203.3/154.8 |
| At engine speed | Rpm | 3500 | 3500 | 3500 | 3500 | 3500 | 3500 | 3500 |
| Max. specific power, |  |  |  |  |  |  |  |  |
| DIN 70020 | kW/l(HP/l) | 46/63 | 43/58 | 43/58 | 63/86 | 55.4/75.6 | 65.5/89.2 | 58/78.6 |
| (SAE J 1349) | kW/l(HP/l) |  | 41/55 |  | 61/82 | 54.6/72.1 | 63.5/85.2 | 55.9/75.1 |
| Fuel octane rating | RON | 98 | 90 | 91 | 98 | 91 | 98 | 91 |
| Max. perm. engine speed | Rpm | 6500 | 6500 | 6500 | 6500 | 6500 | 6500 | 6500 |
| Idle speed | Rpm | 950±50 | 950±50 | 750...800 | 900 ± 50 | 900 ± 50 | <900 | <900 |
| Engine weight (dry) | Kg | 136 | 142 | 142 | 165 | 165 | 165 | 165 |

Technical Data Type 924 Engine Type XK/XJ

Engine design

| Design Crankcase Crankshaft Connecting rods Pistons Camshaft Camshaft drive Cylinder head Valve arrangement Valve timing Valve play Timing with engine warm Intake opens Intake closes Exhaust opens Exhaust closes Engine cooling Engine lubrication Oil filter Oil pressure at 5000 rpm Oil pressure indicators Oil consumption l/1000 km Exhaust system | 4-cylinder,4- stroke spark-ignition engine, in line 1 -piece gray cast iron cylinder/crank- case with aluminum oil pan forged, 5 plain bearings Forged steel Cast light-alloy Case-hardened steel without bearing shells, running in cylinder head by means of toothed belt, with tightening roller Light alloy 1 intake, 1 exhaust in line overhead by overhead camshaft and bucket tappets Intake 0.20 mm, Exhaust 0.45 mm (1 mm stroke, zero play) 6 degr. Before TDC 42 degr. After BDC 47 degr. Before BDC 2 degr. After TDC closed coolant system Forced oil circulation system with crescent pump in full flow approx. 7 bar for oil temperature between 80... 100° С Indicator lamp and pressure gauge up to 1.5 Manifold, single pipe up to front muffler, front, center and final muffler |
| --- | --- |
| Heater Fuel system Fuel delivery Fuel grade RON Fuel consumption Electrical system Interference suppression Battery voltage V Battery capacitance Ah Alternator/output A/W Ignition Ignition sequence Ignition timing Spark plugs Electrode gap mm Power transmission Clutch Pressure plate | Warm water heater with heat exchanger and blower K-Jetronic 1 electric fuel delivery pump 98 Refer to "Operating Instructions" ECE-R 10 and 72/245/EWG 12 45 (opt. Extra 63) 75/1050 Battery ignition system/TSZ ignition system 1-3-4-2 10° CA before TDC at 950 ± 50 rpm without vacuum pipe Bosch W5D, Beru 14-5 DU 0.7 ± 0.1 Front-mounted engine, transmission mounted at rear end, bolted together by a connecting tube to form a rigid drive unit transaxle. Front engine, clutch, torsionally elastic drive shaft to transmission mounted in connecting tube, rear transmission interlocked with axle drive, twin drive shaft to rear wheels. Single-disk dry clutch with disk spring, in compact design, arranged at engine end (MF215K) |

Technical Data for the 924 Carrera GT

Main data of the 924 Carrera GT model 81 compared with the basic 924 turbo

| Engine type |  | 924 Carrere GT M31/5O | 924 turbo M31/03 |
| --- | --- | --- | --- |
| Max. engine power | kW/HP | 154/210 | 130/177 |
| at engine speed | rpm | 6000 | 5500 |
| max. torque | Nm/kpm | 280/28.5 | 250/25.5 |
| max. specific power | kW/l, HP/I | 77.6/105.8 | 65.5/89.2 |
| Engine weight | kg | 175 | 165 |
| Boost pressure | bar | 0.75 | 0.64 |
| Clutch contact force | N | 7800...8500 | 7200...7900 |
| Clutch disk |  | TD225 | GUD 225 |
| Stabilizer, rear | ( | 16mm | 14mm |

Wheels and tires

| 924 Carrera GT | Wheels | Tires |
| --- | --- | --- |
| 5-hole wheels | LMgs7Jx15 | 215/60 VR 15 |
| Rim offset 23.3 mm (924 turbo 53 mm) |  |  |

Engine number code 924 Carrera GT

31 50 0001 -9999        Europe/RoW

Transmission number code 924 Carrera GT

31 03 00001 (12) - 99999     G31/03 - 5-speed Europe/RoW

with differential lock

Torque Specifications - Engine 924/924 turbo

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Bearing housing to crankcase | M12 | 80 (59) |
| Bearing housing 5 to crankcase | M10 | 65(48) |
| Connection rod bolted joint | M10x1 | 60(44) |
| Oil suction line to crankcase | M6 | 10(7.5) |
| Oil drain line to crankshaft bearing housing | M6 | 10(7.5) |
| Housing to oil pump | M 6 | 8(6) |
| Oil pump to crankcase | М6 | 10(7.5) |
| Oil pan to crankcase | M8 | 15(11) |
| Oil pan to crankcase | M6 | 8(6) |
| Oil drain screw | M26 x 1.5 | 40(29) |
| Flywheel to crankshaft | M12x1.5 | 100 (74) |
| Toothed belt pulley to crankshaft | M16X1.5 | 250 (184) |
| V-belt pulley to toothed belt pulley | M8 | 20(15) |
| Water pump to crankcase | M8x72 M8x65 | 22(16) |
| Water pump to crankcase | M6x35 M6x45 | 9(7) |
| Water pump pulley to hub | M8x12 | 20(15) |
| Connection piece to oil pan | M26X1.5 | 110(81) |
| Oil return line from turbo-charger to oil pan |  | 95(70) |
| Oil return line from turbocharger to bracket |  | 85 (63) |
| Screw connector oil filter to oil filter bracket | ¾ -16 UNF | To firm fit max. 20 (15) |
| Bracket for oil filter to crankcase | ¾ -16 UNF-2 В | 60 (44) |
| Oil lines to bracket for oil filter | M18X1.5 | 55 (41) |
| Oil supply line to bracket for oil filter |  | 85 (63) |
| Oil line to bracket for turbocharger |  | 40 (29) |
| Connecting piece to bracket for turbocharger | M14X-1.5 | 40.. .45 (29...33) |
| Camshaft bearing housing to cylinder head | М6 | 10(7.5) |
| Camshaft bearing housing to cylinder head | М8 | 16...20(12...15) |
| Cylinder head cover to cylinder head | М6 | 8(6) |
| Oil pressure sensor to cylinder head | M10x1 | 15(11) |
| Toothed belt gear | М12Х1.5 | 80 (59) |
| Tensioning roller thermostat housing | М10 | 40 (29) |
| Flange for heater on cylinder head | М6х35 | 10 (7.5) |
| Coolant governor | М6 | 10 (7.5) |
| Coolant governor to cylinder head | М8х35 М8х25 | 20(15) |
| Spark plug | M14 x 1.25 | 30(22) |
| Distributor bolts | М8 | 20...22(15...16) |
| Telethermometer transmitter | M10x1 | 8(6) |
| Suction pipe and hoisting bracket to cylinder head | M8x72 М8 | 24(18) |
| Exhaust manifold to cylinder head | М8 | 25(18) |
| Toothed belt cover to cylinder head | M6x25 | 10(7.5) |
| Toothed belt cover to oil pump | M6x25 | 10(7.5) |
| Throttle valve connector piece to suction line | M8x40 | 22(16) |
| Engine bracket to engine nock | М10 | 42(31) |
| Engine mounting to engine bracket | M12x1.5 | 61(45) |
| Engine mounting to frame | М10 | 42(31) |
| Clutch housing to engine | M12 | 75(55) |
| Clutch housing to engine | М10 | 45 (33) |
| Insulating connector piece to cylinder head |  | 22...25(16...18) |
| Injection valve to insulating connector piece |  | 6.0...7.0 (4.5...5.0) |
| Fuel lines to mixture control unit | M12x1.5 | 20(15) |
| Injection lines to injection valve |  | 10(7.5) |
| Injection lines cyls. 1-4 to mixture control unit | M8x1 | 9(7) |
| Fuel line to warm-up regulator and mixture control unit warm-up regulator | M8x1 | 9(7) |
| Fuel line to warm-up regulator |  | 14(10) |
| Fuel line to cold-start nozzle and mixture control unit | M8x1 | 9(7) |
| Fuel line for timing valve to mixture control unit | M8x1 | 9(7) |
| Fuel line to timing valve |  | 12.5 (9) |
| Oxygen sensor to front of exhaust pipe |  | 50...60 (37...44) |
| Control line to bypass valve | M12x1.5 | 20(15) |
| Screw plug to bracket for oil filter | M42X1.5 | 120 (88) |
| Oil filter |  | 20(15) |
| Turbocharger turbine casing | M6 M8 | 12(9) 25(18) |
| Turbocharger compressor casing |  | 7(5) |
| Exhaust manifold flange Turbo charger | M10 | 35(26) |
| (from model year 81 ) | M10 | 50(37) |
| Boost pressure safety switch | M10xl | 15(11) |
| Vent casing on bypass valve | M12x1.5 | 20(15) |

Coat all threads of exhaust system with Optimoly HT

| Tolerances and Wear Limits | when installed (new) | wear limit |
| --- | --- | --- |
| Cooling system Coolant thermostat | Open. Temperature 80...93(C or 85...102(C |
| Cap for cooling system Pressure relief valve Vacuum valve | opens at overpress 0.9...1.15bar opens at vacuum p ress. 0.06...0.1 bar |
| Oil circuit Oil consumption | l/1000 km |  | 1.51 |
| Oil pressure (only for SAE 20 W/20 oils) |  |  |  |
| at 80°С oil temperature: at 2000 rpm | Overpress. | 3...6 bar | 2.0 bar |
| Oil dipstick upper mark | oil content | 5.001 |  |
| lower mark | oil content | 3.801 |  |
| Oil pump: |  |  |  |
| Casing/gear wheels | Axial play | 0.03...0.07 |  |
| Gearwheels | Backlash of teeth | 0...0.13 |  |
| Oil filter: |  |  |  |
| Bypass valve opens | Overpress. | 2.2...3.2 bar |  |
| Oil pressure switch opens at | Overpress. | 0.3...0.6 bar |  |
| Valve timing Bore for camshaft | Inner diameter | 26.00...26.021 |  |
| Camshaft | Diameter | 25.94...25.96 |  |
| Camshaft | Axial play | 0.05. ..0.16 | 0.2 |
| (Measured on center bearing, | Runout |  | Max. 0.02 |
| bearings 1 and 5 on prisms |  |  |  |
| Bore for bucket tappet | Inner diameter | 38.5. ..38.525 |  |
| Bucket tappet | Diameter | 38.45...38.47 |  |
| Cylinder head with valves |  |  |
| Mounting face valve seat: | Distortion |  | max. 0.1 |
| a) Intake | Width | 2.0 |  |
| b) Exhaust | Width | 2.4 |  |
| c) Intake | Seating angle | 45° |  |
| d) Exhaust | Seating angle | 45° |  |
| Valve guides |  |  |  |
| Intake and exhaust | Inner diameter | 9.000...9.015 |  |
| Valve stem: |  |  |  |
| Intake | Diameter | 8.97 |  |
| Exhaust | Diameter | 8.95 |  |
| Valve guide/valve stem | Play |  |  |
| Intake |  | 0.4 | 0.8 |
| Exhaust Compression | Overpress. | 0.5 8...11 bar | 1.0 6 bar |
| Pressure difference between individual cylinders | in |  | max. 3 bar |
| Pistons with connecting rode |  |  |
| Cylinder/piston | Play | 0.03 | 0.08 |
| Cylinder/piston 924 turbo | Play | 0.048...0.072 | 0.12 |
| Weight difference of an engine's pistons | for repairs |  | max. 14g |
| Piston rings | Vert. play | 0.04...0.07 . | 0.1 |
| Piston rings | Gap width | О.3...0.5 | 1.0 |
| Con rod weight | Standard | 815...927g |  |
| Weight difference of an |  |  |  |
| engine's con rods | new | Eg |  |
|  | for repairs | 8g |  |
| Con rod bush | Diameter | 24.012...24.018 |  |
| Piston pin | Diameter | 23.996...24.000 |  |
| Con rod bush/piston pin | Radial play | 0.01 ...0.02 |  |
| Crankshaft and cylinder block |  |  |
| Crankshaft (measured on 2nd, 3rd or | Runout |  | max. 0.06 |
| 4th bearing, bearings 1 and 5 on prisms) |  |  |  |
| Con. rod journal | Diameter | 47.95...47.97 |  |
| Con rod/crankshaft | Radial play Axial play | 0.02...0.07 0.05...0.08 | 0.1 0.4 |
| Crankshaft bearing journal | Diameter | 59.95...59.97 (63.95. ..63.97*) |  |
| Crankshaft bearing/ crankshaft | Radial play | 0.02...0.08 | 0.16 |
| Crankshaft bearing 3/ crankshaft | Axial play | 0.1 ...0.19 | 0.25 |
| Cylinder bore | out-of-round |  | 0.04 |
| Cylinder block/crank- shaft bearing bore | Diameter | 68.000...68.019 |  |
| 924turbo |  |  |  |
| Turbocharger | Radial play |  | max. 0.42 |
| Turbocharger | Axial play |  | max. 0.16 |

Repair Stages for Crankshaft (Dimensions in mm)

(from engine no. XK 00 32 14)

|  | Crankshaft bearing Journal |  | Crankshaft con rod Journal |  |
| --- | --- | --- | --- | --- |
|  | Journal | ( | Max. out-of-round | Journal | ( | Max. |
| Original size | 64.OO: | -0,03 -0,05 | 0.03 | 46.00 | -0,03 -0,05 | 0.03 |
| Repair stage I | 63.75: | -0,03 -0,05 | 0.03 | 47,75 | -0,03 -0,05 | 0.03 |
| Repair stage II | 63.50: | -0,03 -0,05 | 0.03 | 47,50 | -0,03 -0,05 | 0.03 |
| Repair stage III | 63.25: | -0,03 -0,05 | 0.03 | 47,25 | -0,03 -0,05 | ' 0.03 |

Permitted vertical runout for crankshaft max. 0.06 mm, measured at main bearings 2, 3 and 4, bearings 1 and 5 on prisms.

Checking Pistons and Cylinder Bores 924

| Checking pistons Measure approx. 16 mm from lower edge, offset 90' to piston pin axis. Deviation from prescribed dimension (see table): max. 0.04 mm |  |
| --- | --- |
| Checking cylinder bores Measure at 3 points, transversely - "A" –and longitudinally - "B". Deviation from prescribed dimension (see table): max. 0.08 mm |  |

| Repair stage | Tolerance group identification | Cylinder bore (mm) | Piston diameter (mm) Mahle pistons/KS pistons |
| --- | --- | --- | --- |
|  | 601 | 86.5 | +0,015 +0,005 | 86.48 ± 0.007 |
| Stand.dmens. | 602 | 86,5 | +0,025 +0,025 | 86.49 ± 0.007 |
|  | 603 | 86.5 | +0,035 +0,025 | 86.50 ± 0.007 |
|  | 626 | 86.75 | +0,015 +0,005 | 86.73 ± 0.007 |
| 1st oversize | 627 | 86.75 | +0,025 +0,015 | 86.74 ± 0.007 |
|  | 628 | 86.75 | +0,035 +0,025 | 86.75 ± 0.007 |
|  | 651 | 87.00 | +0,015 +0,005 | 86.98 ± 0.007 |
| 2nd oversize | 652 | 87.00 | +0,025 +0,015 | 86.99 ± 0.007 |
|  | 653 | 87.00 | +0,035 +0,025 | 87.00 ± 0.007 |

The tolerance group identification is stamped into the cylinder block on the starter motor side, just under the cylinder head.

Checking Pistons and Cylinder Bores 924 turbo

| Checking pistons Measure approx. 13 mm from lower edge, offset 90° to piston pin axis. Deviation from prescribed dimension (see table): max. 0.04 mm |  |
| --- | --- |
| Checking cylinder bores Measure at 3 points, transversely - "A" –and tongitudinally - "B". Deviation from prescribed dimension (see table): max. 0.08 mm |  |

| Repair stage | Marking on piston head | Piston ( (mm) | Cylinder bore (mm) | Tolerance group identification |
| --- | --- | --- | --- | --- |
| Stand. dimension | 86.5 ¦ ¦¦ ¦¦¦ | 86.45 86.46 86.47 | 86.51 86.52 86.53 | 601 602 603 |
| 1st Rep. stage | 86.75 ¦ ¦¦ ¦¦¦ | 86.70 86.71 86.72 | 86.76 86.77 86.78 | 626 627 628 |
| 2nd Rep. stage | 87.0 I ¦¦ ¦¦¦ | 86.95 86.96 86.97 | 87.01 87.02 87.03 | 651 652 653 |
| 3rd Rep. stage | 87.5 I ¦¦ ¦¦¦ | 87.45 87.46 87.47 | 87.51 87.52 87.53 | 701 702 703 |

Note

Only pistons from a single manufacturer (Mahle or KS) may be used in one and the same engine.

#### Valve Dimensions

| 924 | 924 turbo |
| --- | --- |
| Intake valve | Exhaust valve | Intake valve | Exhaust valve |
| a) (40mm | ( 33mm | ( 40mm | ( 36 mm |
| b) (8.97 mm | ( 8.95 mm | ( 8.97 mm | ( 8.95 mm |
| c) 137.2mm | 136.95 mm | 133.2 mm | 133.35 mm |
| d) 2.2...3.0 mm | 2.2...3.0 mm | 2.2...3.0 mm | 2.2...3.0 mm |
| ( 45° | 45° | 45° | 45° |

Checking Valve Guides

Insert new valve into guide until valve stem end is flush with end of guide. Ascertain play.

Wear limit for intake valve guide            0.8 mm

Wear limit for exhaust valve guide           1.0 mm

Adjusting Screw Notching

The number of notches indicates the thickness of the valve adjusting screws.

Higher number of notches = thicker adjusting screw

| New adjusting screw Part no. | Identification |  |
| --- | --- | --- |
| 046.109.453.D 046.109.453.E 046.109.453 F 046.109.453 G 046.109.453 С | 1 notch 2 notches 3 notches 4 notches without notch | The replacement adjusting screw will continue to be available, but without any marking (previously white dot of paint). |

Checking and Adjusting Valve Play Reworking Intake Valves

| Valve play is checked and adjusted with the engine at operating temperature (oil temp. approx. 80°C.) |  |
| --- | --- |
| Intake valve: 0.20 mm Exhaust valve: 0.45 mm |  |
| Basic valve play setting (for engine overhaul etc.) |  |
| With engine cold Intake valve: 0.10mm Exhaust valve: 0.40 mm | When reworking the valve, dimension a = 3.5 mm must not be exceeded. Note Exhaust valves must not be reworked. Only grinding to size is permitted. |

Reworking Valve Seats

Valve seats with traces of wear or burning may be reworked until the wear limit "b" is reached. If the wear limit is exceeded, the cylinder head should be replaced, as the prescribed valve play can no longer be set, and valve seat rings cannot be replaced using conventional workshop equipment.

924

Intake valve seat           Exhaust valve seat

a) ( 38.5 mm                  a) ( 31.5 mm

b) max. 3.3 mm              b) max. 3.9 mm

Caution

If a valve seat has been reworked, the valve adjusting screw of the bucket tappet belonging to that valve must be exchanged for a replacement adjusting screw, 046 109 453 С (without marking).

924 turbo

New dimension, measured from cylinder head mating face to valve head:

Intake  5.0mm Wear limit:                  Intake 5.3mm

Exhaust 4.7mm                            Exhaust 5.2 mm

Carry out check with new valve. Keep material loss to a minimum.

Tightening Specifications - Cylinder Head Bolts • 924

Tightening sequence for cylinder head

Tightening specifications using the turning angle method-924-inductlon engine

Tightening is performed in two stages, following the sequence shown in the diagram at each stage. Reverse sequence when undoing the bolts.

Turning angle tightening method

Tightening in two stages (with screws with internal serrations)

1st stage                65 Nm

2nd stage               180°= 1/2 tum

Tightening specifications for cylinder head bolts - 924 turbo

1. Tighten cylinder head bolts in prescribed sequence, in stages, to 40 Nm, 80 Nm and 110 Nm.

2. Retighten cylinder head bolts after at least 60 minutes (to allow for settling of cylinder head). To do so, loosen bolt no. 1 (see tightening sequence) approx. ½ a turn and tighten to 110 Nm. Repeat this procedure with the remaining bolts in the prescribed sequence. Bring engine up to operating temperature (oil temperature approx. 80° С). Allow engine to cool and give cylinder head bolts a final tightening as described under 2.

Machining the Cylinder Head Mating Face

Permissible unevenness of mating face: 0.1 mm

Max. reworking depth 0.4 mm

Peak-to-valley height = 0.015 mm

Size Worn A = 139.55mm

Main Testing and Adjusting Values for Engine

| Engine type 924 | Engine type 924 turbo |
| --- | --- |
|  | XK,XJ | XG,XE | VC |  | M31/D1/02 | M31/03/04 | Mod. 81 (Sweden, Australia) |
| Electric fuel pump Delivery rate | Min. 750 cm3/30 s | as XK, XJ | as XK, XJ | Electric fuel pump Delivery rate | min. 1050cm3/30s | as 01/02 | as 01/02 |
| System pressure test value | 4.5...5.2 bar | as XK, XJ | as XK, XJ | System pressure test value | 5.8...6.5 bar | as 01/02 | as 01/02 |
| Adjust, value | 4.7...4.9 bar | as XK, XJ | as XK, XJ | Adjust, value | 6.0...6.3 bar | as 01/02 | as 01/02 |
| Control pressure cold (approx. 20° C) | 1.3...1.7bar | as XK, XJ | 1.7...2.1 | Control pressure cold (approx. 20° C) | 2.0...2.4 bar | 2.4...2.8 | 1.3...1.7 |
| Control pressure warm | 3.4...3.8 bar | as XK, XJ | as XK, XJ | Control pressure warm without overpressure | 3.45...3.85 bar | as 01/02 | 3.1 ...3.5 |
| Leakiest |  |  |  | Leak test |  |  |  |
| Min. pressure after 10 min. | 1.7 bar | as XK, XJ | as XK, XJ | Min. pressure after 10 min. | 2.0 bar | as 01/02 | as 01/02 |
| Min. pressure after 20 min. | 1.5 bar | as XK, XJ | as XK, XJ | Min. pressure after 20 min. | 1.7 bar | as 01/02 | as 01/02 |
| Opening pressure of inject valves | 2.5...3.6 bar | as XK, XJ | as XK, XJ | Opening pressure of injection valves | 2.7...3.8 bar | as 01/02 | as 01/02 |
| Ignition timing with vacuum hose disconnected | 10° CA before TDC for 950 ± 50 rpm |  |  | Ignition timing with vacuum hose disconnected | M31/01 25° CA before TDC at 2000 rpm M31/02 20° CA before TDC at 2000 rpm | Digital advance unit (DZV) |  |

| Ignition timing with vacuum hose connected |  | 3° CA after TDC for 950 ± 50 rpm | 0° CA = TDC for 950 ± 50 rpm |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| Test | Testing and Adjusting values 924 | Special notes |
| --- | --- | --- |
| Idle speed setting Idle speed rpm | 950 ± 50 rpm 750...800 rpm (from mod. 81 USA, California, Canada) 1000 + 50 rpm (from mod. 81, Japan, automatic) | All consumers switched off |
| CO content % | 1.0...2.0% USA and Canada Mod. 78 0.5... 1.0 % * (measured upstream of cat.) Mod. 79 0.7... 1.1 % * (measured upstream of cat.) Mod. 80 0.6...1.0 % (measured upstream of cat.) from mod. 81 0.5...1.0 % (measured upstream of cat.) | *Air pump and activated charcoal container not connected Plug connector for oxygen sensor not connected |
|  | California Up toMod.79 max. 0.7 %* (measured upstream of cat.) Mod. 79 0.8... 1.2 %* (measured upstream of cat.) Mod. 80 0.6...1.0 % (measured upstream of cat.) Frommod.81 0.5...1.0 % (measured upstream of cat.) | Plug connector for oxygen |
|  | Japan Mod. 78 0.5...1.0 %* (measured upstream of cat.) Mod. 79 0.7... 1.1 %* (measured upstream of cat.) Mod. 80 0.6....1,0 % (measured upstream of cat.) From mod. 81 0.6... 1.0 % (measured upstream of cat.) | Plug connector for oxygen sensor not connected |
| Test | Testing and Adjusting Values 924 turbo (GT) | Special notes |
| Idle speed setting |  | from mod. 81 (DZV ignition system) with cold intake airtemp. Sensor |
| Idle speed rpm | 900 ± 50 rpm Mod. 79/80 (Europe, USA, Japan and Canada) < 900 rpm from mod. 81 | ignition marking in insp. aperture |
| CO content % | 0.5...1.0 Mod. 79/80 (Europe, USA, Japan and Canada) 0.5...1.5 from mod. 81 1.0. ..2.0 Australia, Sweden | measured upstream of cat., plug connector for oxygen sensor not connected |

Measuring Boost Pressure 924 turbo

| Model 79/80 | from Model 81 |
| --- | --- |
| Europe USA | Europe USA |
| 0.67...0.73bar 0.43...0.47bar | 0.62...0.68 bar 0.43...0.47 bar |

924 Саггега GT 0.72...0.78 bar

V-Belt Dimensions

| 924 V-belt for alternator | mm 9.5 x 888 LA without teeth |
| --- | --- |
| V-belt for alternator as from mod. 81 | mm 9.5 x 888 LA with teeth |
| V-belt for air-conditioning compressor | mm 12.5х900 LA without teeth |
| V-belt for compressor as from mod. 79 | mm 13/12.5 x 875 la with teeth |
| V-belt for air pump (air injection) | mm 9.5 x 771 LA |
| 924turto V-belt for alternator as from mod. 81 | mm 9.5 x 1048 LA without teeth mm 9.5 x 1050 LA with teeth |

Coolant Mixing Table

| Frost protection to | Antifreeze | Water | Antifreeze | Water |
| --- | --- | --- | --- | --- |
| -25°С | 40% | 60% | 2.81 | 4.21 |
| -30°C | 45% | 55% | 3.21 | 3.81 |
| -35°С | 50% | 50% | 3.51 | 3.51 |

Page Transmission and clutch

Torque Specifications Manual Transmission, Central Tube, Clutch and Actuating Elements 924 (4-speed transmission type 088)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Side transm. Flange | M8 | 25(18) |
| Side transm. cover | M8 | 27 (20) |
| Cover for shifting shaft | M6 | 8(6) |
| End shield | M8 | 24(18) |
| Drive shaft | M8 | 24 (18) |
| Drive shaft | M8 | 24(18) |
| Oil filler screw | M24 | 25(18) |
| Oil drain screw | M24 | 25(18) |
| Reverse gear pin | M8 | 25(18) |
| Reversing lever bearing | M10X1.5 | 35(26) |
| Shifting lock | M14X1.5 | 30(22) |
| Reversing lever | M18x1.5 | 30(22) |
| Crown gear | M10x1 | 85...100 (63...74) |
| Flanged shaft to diff. gear | M8 | 25(18) |
| Protective tube to transmission case | M7 | 10...16 (7.5...12) |
| Joint shaft | M8 | 42(31) |
| Shifting lever mounting | M8 | 21 (15) |
| Joint rod to intermediate shifting lever | M8 | 21 (15) |
| Joint rod to transmission case | M8 | 14(10) |
| Reversing light switch | M18x1.5 | 30(22) |
| Exhaust line to transmission | M10 | 45(33) |
| Exhaust line to Transaxle system | M8 | 10 (7.5) |
| Front muffler to exhaust pipe | M8 | 20(15) |
| Central tube housing to transmission case | M12 | 85 (63) |
| Central housing to transmission case | M10 | 42(31) |
| Shift lever plate to central tube | M8 | 21 (15) |
| Central shaft to transmission shaft | M8x35 | 30 (22) |
| Central tube flange to clutch housing | M10X35 | 42(31) |
| Clutch housing to engine flange | M10x1.5 M12x1.5 | 45 (33) 75(55) |
| Transmission bearing to body | M10 | 42(31) |
| Bearing bracket to transmission | M8 | 25(18) |
| Clutch lever | M8 | 15(11) |
| Clutch to flywheel | M8 | 32 (24) |
| Guide tube to clutch housing | M7 | 10...16(7.5...12) |
| Support strut to tans-mission (USA) | M10 | 42 (31) |
| Arrester to central tube (USA) | M8 | 20(15) |

Torque Specifications - Manual Transmission, Central Tube, Clutch and Actuating Elements 924 (5-speed transmissions type 016 Z and 016 Y)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Drive shaft | M30 x 1.5 | 220...240 (161 ...175) |
| Drive shaft | M22 x 1.5 | 160...180 (110...133) |
| Driving shaft | M24 x 1.5 | 200...220 (147...162) |
| Flange shaft to diff. gear | M10X1.5 | 47...50 (35...37) |
| Shift lock/rear axle and wheel housing | M10X1.5 | 15...18 (11 ...13) |
| Mounting of casing and cover | M8х1.25 | 22...25(16...18) |
| Crown gear/diff. Gear | M12 x 1.25 | 150...160 (111 ...118) |
| Locking pawl/rear axle casing | M6x1 | 8...10(6...7.5) |
| Reversing light switch/ wheel housing | M18X1.5 | 25...32 (18...24) |
| Oil filler screw/wheel housing | M24 x 1.5 (tapered) | 20...25 (15...18) |
| Oil drain screw/rear axle casing | M25X1.5 (tapered) | 20...25(15...18) |
| Tension plate, rear axle casing, wheel housing | M8х1.25 | 22...25(16...18) |
| Joint shaft | M8 | 42(31) |
| Exhaust tine to transmission | M10 | 45(33) |
| Exhaust line to transaxle system | M8 | 10(7.5) |
| Front muffler to exhaust pipe | M8 | 20(15) |
| Central shaft to transmission shaft | M8x35 | 35 (26) |
| Central tube flange to clutch housing | M10X35 | 42 (31) |
| Clutch housing to engine flange | M10x1.5 M12x1.5 | 45(33) 75(55) |
| Clutch lever | M8 | 15(11) |
| Clutch to flywheel | M8 | 32 (24) |
| Guide tube to clutch housing | M7 | 10...16 (7.5...12) |
| Transmission bearing to transmission | M10 | 42(31) |
| Transmission bearing to rear axle transverse tube | M10 | 42(31) |
| Central tube to transmission case | M12x1.5 | 85 (63) |
| Shifting rod to inner shifting rod/transmission | M8 | 18(13) |
| Bearing bracket to floor unit - center | M6 | 9(7) |
| Angled linkage to guide rod | BM10 | 23(17) |

Torque Specifications - Manual Transmission, Central Tube, Clutch and Actuating Elements 924 (5-speed transmissions type 016/8 and 016/9)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Oil filler screw to transmission case | M24 | 25(18) |
| Oil drain screw to transmission case | M24 | 25(18) |
| Protective tube to transmission case | M7 | 10...16 (7.5...12) |
| Shifting shaft to transmission case | M6 | 6...10(4.5...7.5) |
| End shield to transmission case | M8 | 24 (18) |
| Ball bearing to drive shaft | M10 | 50(37) |
| Cover to end shield | M8 | 25(18) |
| 5th gear wheel to driving shaft | M10 | 50 (37) |
| Shifting lock to end shield | M18 | 30 (22) |
| Shift travel limiter to | M18 | 30(22) |
| End shield | M14 |  |
| Reverse transfer lever to end shield | M10 | 35(26) |
| Reverse gear pin to end shield | M8 | 20(15) |
| Flanged shaft to diff. gear | M8 | 25(18) |
| Side transmission cover to transmission case | M8 | 25(18) |
| Crown gear to diff. casing | M10 | 85...100 (63...74) |
| Reversing light switch to transmission case | M18 | 30(22) |
| Joint shaft | M8 | 42(31) |
| Joint rod to transmission case | M8 | 21 (15) |
| Joint rod to transmission case | M8 | 14 (10) |
| Shift lever plate to central tube | M8 | 21 (15) |
| Exhaust line to transaxle system | M8 | 10(7.5) |
| Front muffler to exhaust pipe | M8 | 20(15) |
| Central tube housing to transmission case | M12 | 85 (63) |
| Central tube housing to transmission case | M10 | 42 (31) |
| Shifting rod mounting | M8 | 21 (15) |
| Central shaft to transmission shaft | M8x35 | 35(26) |
| Central tube flange to clutch housing | M10x35 | 42(31) |
| Clutch housing to engine | M10x1.5 M12x1.5 | 45(33) 75(55) |
| Clutch bearing to body | M10 | 42(31) |
| Bearing bracket to transmission | M8 | 25(18) |
| Clutch lever | M8 | 15(11) |
| Clutch to flywheel | M8 | 32(23) |
| Guide tube to clutch housing | M8 | 10...16 (7.5...12) |

Clutch 924

| Design Pressure plate Contact pressure Clutch disk Clutch drive plate with riveted on lining Thickness untensioned (new) Wear limit Lateral runout Clutch play at clutch pedal | Single-plate dry clutch with disk spring, compact design MF215K 4810.. .5490 N (215mm 10.1-0.4 mm 8.5 mm with asymmetrical wear Max. 0.6 mm with ( 2OO mm 20-25 mm |
| --- | --- |

Clutch 924 turbo

| Design Pressure plate Contact pressure Clutch disk Clutch drive plate with riveted on lining Thickness untensioned (new) Wear limit Lateral runout Clutch play at clutch pedal | Single-plate dry clutch with disk spring, hydraulically actuated, extended design MFZ225 7200.. .7900 N ( 225 mm 8.1 ± 0.3 mm 6.3 mm with asymmetrical wear Max. 0.6 mm with ( 225 mm Approx. 3 mm |
| --- | --- |

Technical Data 4-Speed Manual Transmission Type 924 YR (924 XT*)

| Ratios 1st gear 2nd gear 3rd gear 4th gear R.gear | 10:36 i=3.60 16:34 i=2.125 25:34 i = 1.360 30:29 i = 0.966 12:42 i=3.50 |
| --- | --- |
| Final drive | Hypoid drive, 12 mm offset |
| Final drive ratio | 9:35 i= 3.8888 |
| Climbing ability in % 1st gear 2nd gear 3rd gear 4th gear | 54 (49.5) 28 (26) 16 (14.5) 9.5 (9) |
| Power transmission | Front engine and transmission (at rear) bolted together by means of a connecting tube to form a rigid drive unit. Front engine, clutch, torsionally elastic shaft (20 mm Ø) to transmission mounted in 4 bearings, rear transmission interlocked with drive axle, twin articulated drive shafts to rear wheels |
| Transmission weight (dry) | 45 kg (99 Ibs) |
| Filling capacity | Approx. 2.6 liters multi-grade transmission oil, SAE 75 W-9O, API classification GL 5 (or MIL-L 2105 В) or 80 W90-GL 4 |

Technical Data 5-Speed Manual Transmission Types 016 Z and 016 Y *

| Ratios 1st gear 2nd gear 3rd gear 4th gear 5th gear R. Gear | 14:39(14:39) i= 2.7857 (2.7857) 18:31 (19:32) i = 1.7222 (1.6842) 23:28(27:30) i= 1.2174 (1.1111) 29:27 (31:25) i = 0.9310 (0.8064) 34:24 (35:21) i = 0.7059 (0.6000) 46:21-16:14 i= 2.5034 |
| --- | --- |
| Final drive | Helical bevel gear differential |
| Final drive ratio | 7:33 i= 4.7143 (7:35 i= 5.000) |
| Power transmission | Front engine and transmission (at rear) bolted together by means of a connecting tube to form a rigid drive unit. Front engine, clutch, torsionally elastic shaft (Ø20 mm) to transmission mounted in 4 bearings, rear transmission interlocked with drive axle, twin articulated drive shafts to rear wheels |
| Getriebegewicht (trocken) | 45 kg (99 Ibs) |
| Filling capacity | Approx. 2.5 liters multi-grade transmission oil, SAE 75 W-9O, API Classification GL 5 (orMIL-L2105B) |
| "Specifications for USA in brackets |  |

Technical Data 5-Speed Manual Transmission Types 016/8 and 016/9 *

| Ratios 1st gear 2nd gear 3rd gear 4th gear 5th gear R. gear Final drive | 10:36 i= 3.600 16:34 i=2.125 24:35 (25:34) i = 1.458 (1.360) 28:31(30:29) i= 1.107 (0.966) 35:30 (37:27) i = 0.857 (0.729) 12:42 i= 3.500 Hypoid drive, 12 mm offset |
| --- | --- |
| Final drive ratio | 9:35(9:37) i= 3.889 (4.111) |
| Climbing ability in % 1st gear 2nd gear 3rd gear 4th gear 5th gear | 59 (57) 32(30) 21 (18) 14(11.5) 9.5(7) |
| Power transmission | Front engine and transmission (at rear) bolted together by means of a connecting tube to form a rigid drive unit. Front engine, clutch, torsionally elastic shaft (Ø 20 mm) to transmission mounted in 4 bearings, rear transmission interlocked with drive axle, twin articulated drive shafts to rear wheels |
| Transmission weight (dry) | 55 kg (121 Ibs) |
| Filling capacity | Approx. 2.5 liters multi-grade transmission oil, SAE 75 W-9O, API Classification GL 5 (or MIL-L 2105 В) or 80 W90-GL4 |
| "Specifications for USA in brackets |  |

Torque Specifications - Automatic Transmission 924

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Oil filler transmission case | M24X1.5 | 20 (15) |
| Flange shaft to differential | M8х1.25 | 25(18) |
| Locking plate to adjusting ring | M6x1 | 8(6) |
| Planetary gear to axle drive | M8х1.25 | 29(21) |
| Governor cover to axle housing | M8х1.25 | 9(7) |
| Cover for diff. pinion to axle housing | M8х1.25 | 25(18) |
| Cover of axle housing to axle housing | M8х1.25 | 25(18) |
| Crown gear to differential | M10x1 | 78...93 (58...69) |
| Governor shaft to governor housing | M5х0.8 | 3.5 (3) |
| Screw plug tor measuring connection | M10x1 | 15(11) |
| Lever for hand slide valve to transmission case | M6x1 | 3.5 (3) |
| Detent segment to lever for hand slide valve | M16X1.5 | 20.5 (15) |
| Lever of kickdown valve to shaft of accelerator rod | M8х1.25 | 17(13) |
| Detent spring to transmission case | M8х1.25 | 20.5 (15) |
| Pump to transmission case | M6x1 | 7.0(5) |
| Slide valve case to transmission case | M6x1 | 3.5(3) |
| Oil strainer to slide valve case | M5х0.8 | 3.5(3) |
| Oil pan to transmission case | M8х1.25 | 20.5 (15) |
| Intermediate plate to transmission case | M5х0.8 | 3.5(3) |
| Facing plate to slide valve case | M5х0.8 | 3.5(3) |
| Supporting plate to duct plate | M5х0.8 | -3.5(3) |
| Intermediate and duct plates to slide valve case | M5х0.8 | 3.5(3) |
| Cover plate to pump housing | M4х0.7 | 1.4(1) |
| Adjustment brake strap 2nd gear | M12X1.5 | 19.6(14) |
| Converter to drive plate | M8 | 21 (15) |

Torque Specifications -Automatic Transmission Actuating Elements 924

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Shift lever guide to shift bracket | M6 | 9(7) |
| Locking segment to shift bracket | M6 | 10 (7.5) |
| Mount of shift actuation and side seal guide | M6 | 10(7.5) |
| Retaining bracket to transmission | M8 | 21 (15) |
| Cable to bracket | M8 | 8±1 (6±1) |
| Cable to retaining bracket | M8 | 8±1(6±1) |
| Cable to transmission lever | M8 | 5±1(4±1) |

Torque Specifications -Accelerator Actuation (Automatic Transmission) 924

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Guide pulley to bracket | M6 | 9(7) |
| Guide pulley bracket to intake pipe | M6 | 9(7) |
| Control cable to bracket | M8 | 5(4) |
| Control cable to transmission | M10 | 30(22) |
| Control cable to central tube | M4 | 1.4(1) |
| Rubber to lever for accelerator actuation | M6 | 9(7) |
| Rubber to lever | M6 | 9(7) |
| Support to bracket for guide pulley | M6 | 9(7) |
| Support for guide pulley to crankcase | M8 | 21 (15) |
| Accelerator pedal to floor plate | M6 | 5(4) |

Torque Specifications-Central Tube (Automatic Models) 924

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Torque converter mounting to rear bell | M8x25 | 21 (15) |
| Mounting of central shaft to flange shaft | M8 | 35 (26) |
| Central tube flange to clutch bell | M10x35 | 42(31) |
| Central tube housing to transmission case | M12X1.5 | 85 (63) |
| Central tube housing to transmission case | M10x-1.5 | 42(31) |
| Torque converter to driver plate | M8x12 | 21(15) |
| Mounting of central shaft to clamper | M8 | 35 (26) |
| Damper to flywheel | M8x18 | 21 (15) |
| Cover to clutch housing | 6.3х19 | 5(4) |
| Stop basket to damper | M8x25 | 21 (15) |

Technical Data - Automatic Transmission 924

| Internal designation | RK(RL) |
| --- | --- |
| Number of speeds | 3 forward, 1 reverse and parking lock |
| Ratios: | Driving position 1 i = 2.5517 Driving position 2 i= 1.4483 Driving position D i=1.0000 Driving position R i= 2.4615 |
| Clutch | Hydrodynamic torque converter |
| Torque converter ratio | 2.2 (up to mod. 79 = 2.1 from mod. 80 = 2.44) |
| Stall speed | 2600 ± 200 (up to mod. 79 = 2100 ± 200 from mod. 80 = 2450 ± 200) |
| Torque conv. code letter | К (up to mod. 79 = J, from mod. 80 = M) |
| Final drive | Hypoid drive set |
| Hypoid offset | 44mm |
| Axle ratio | 11/38(11/41) |
| Filling capacities Final drive | approx. 11 multi-grade gear oil, SAE 75 W-90, API classification GL 5 (or MIL-L 2105 В) |
| Automatic section | 61 total filling capacity with ATP Dexron, torque converter capacity 2.51, change quantity approx. 2.81, observe marking on top-up reservoir |

Specifications for USA in brackets

Pressure-Testing Hydraulic Control Unit

| Up to model 80 | From model 81 |
| --- | --- |
| Selector Lever. Pos. | Accel. pedal pos. | Main press. In bar Overpressure (kg/cm2) | Test con-dition | Selector lever pos | Accel.. pedal pos. | Main press. In bar Overpressure (kg/cm') | Test-condition ) |
| D | Idle (zero accel.) | 2.95 ± 0.05 |  | D | Idle (zero accel.) | 2.95 ± 0.05 |  |
|  |  |  | Speed more than 50 km/h* |  |  |  | Speed more than 50 km/h* |
| D | Full accel. | 6.85 ± 0.05 (590+005) |  | D | Full accel. | 6.85 ± 0.05 (5,90 ± 0,05) |  |
| R | Idle (zero accel.) | 7.35 ± 0.3 | Vehicle stationary | R | Idle (zero accel.) | 9.6 ± 0.3 (9.4 ± 0.3) | Vehicle stationary |
| R | Full accel. | over 18 | at stall speed | R | Full accel. | over 18 | at stall speed |

•Specifications for USA in brackets

Torque Specifications - Manual Transmission 924 turbo (Types G31/01, G31/02, G31/03)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Drive shaft | M 30 x 1.5 | 220 (162) |
| Driving shaft | M 24 x 1.5 | 220 (162) |
| Flange shaft to diff. gear | M10x1.5 | 46(34) |
| Shift lock/rear axle and wheel housing | M10x1.5 | 18(13) |
| Mounting of casing and cover | M 8х1.25 | 25(18) |
| Crown gear/diff. gear | M 12 x 1.25 | 150(111) |
| Locking pawl/rear axle casing | M6x1 | 10 (7.5) |
| Reversing light switch/ wheel housing | М18х1.5 | 30(22) |
| Oil filler screw/wheel housing | М24Х1.5 (tapered) | 25(18) |
| Oil drain screw/rear-axle casing | М25х1.5 (tapered) | 25(18) |
| Tension plate, rear axle casing, wheel housing | M 8х1.25 | 25(18) |
| Joint shaft to joint flange | M 8х1.25 | 42(31) |

Torque Specifications - Clutch, Central Tube, Transmission Suspension, Shift Actuation 924 turbo (Type G31/01, G31/02, G31/03)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Clutch |  |  |
| Guide tube to clutch housing | M7 | 12(9) |
| Clutch and ring gear mounting | M8 | 25(18) |
| Flywheel to crankshaft | M12 | 100 (74) |
| Clutch housing to engine | M12 M10 | 75(55) 45 (33) |
| Clutch release shaft with clutch casing | M6x35 M6 | 9.5 (7) 7.5(5) |
| Clutch operating cylinder to clutch housing | M8x28 | 21 (15) |
| Central tube |  |  |
| Central shaft to transmission input shaft | M10x46 | 80 (59) |
| Central tube flange to clutch housing | M10x35 | 42(31) |
| Central tube flange to transmission case | M12 | 85 (63) |
| Transmission suspension |  |  |
| Transmission bearing to rear axle transverse tube | M10 | 42(31) |
| Transmission bearing to transmission | M10 | 42(31) |
| Shift actuation |  |  |
| Bearing support to center of floor unit | M6x10 | 9(7) |
| Shifting rod to transmission | M8 | 18(13) |
| Angled joint to guide rod | BM 10 | 23(17) |

Torque Specifications - Manual Transmission 924 turbo (Type 016G)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Oil filler screw to transmission case | M24 | 25(18) |
| Oil drain screw to transmission case | M24 | 25(18) |
| Cover for shifting shaft to transmission case | M6 | 6...10 (4.5...7.5) |
| End shield to transmission case | M8 | 24(18) |
| Bait bearing to transmission input shaft | M10 | 50 (37) |
| Cover to end shield | M8 | 25(18) |
| 5th gear wheel to driving shaft | M10 | 50(37) |
| Shifting lock to end shield and transmission case | M18 | 30(22) |
| Shift travel limiter to end shield | M18 M14 | 30(22) |
| Reverse-transfer lever to end shield | M10 | 35(26) |
| Reverse gear pin to end shield | MS | 20(15) |
| Flange shaft to differential | M8 | 25(18) |
| Transmission side cover to transmission case | M8 | 25(18) |
| Crown gear to differential casing | M10 | 85...100 (63...74) |
| Reversing light switch to transmission case | M18 | 30 (22) |
| Joint shaft to joint flange | M8 | 42(31) |

Torque Specifications - Clutch, Central Tube, Transmission Suspension and Shift Actuation 924 turbo (Type 016G)

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Clutch Guide tube to clutch housing | M7 | 12(9) |
| Clutch and ring gear mounting | M8 | 25(18) |
| Flywheel to crankshaft | M12 | 100 (74) |
| Dutch housing to engine | M12 M10 | 75(55) 45(33) |
| Clutch release shaft with clutch housing | M6x35 M6 | 9.5 (7) 7.5 (5) |
| Clutch operating cylinder to clutch housing | M8x28 | 21 (15) |
| Central tube |  |  |
| Central shaft to transmission input shaft | M10x46 | 80 (59) |
| Central tube flange to clutch housing | M10x35 | 42(31) |
| Central tube housing to transmission housing | M12x75 M12x80 M10X60 | 85(63) 85(63) 42(31) |
| Transmission suspension |  |  |
| Transmission bearing to body | M10 | 42(31) |
| Bearing to support bracket | M8 | 23(17) |
| Support bracket to | M8 | 25(18) |
| Transmission Shift actuation |  |  |
| Joint rod to transmission case | M8 | 14(10) |
| Joint rod to intermediate shifting lever | M8 | 21 (15) |
| Shifting rod mounting | M8 | 21 (15) |
| Shift lever plate to central tube | M8x12 | 21 (15) |
| Intermediate shifting lever to shifting shaft | M8 | 22.5 (17) |

Technical Data- 5-Speed Manual Transmission G 31/01, G31/02* and G31/03

| Ratios 1st gear 2nd gear 3rd gear 4th gear 5th gear R.gear | 10:36 i= 3.6000 16:34 i= 2.1250 24:35 i=1.4583 28:31 i=1.1071 37:27 i = 0.7297 12:42 i= 3.5000 |
| --- | --- |
| Final drive | Hypoid drive, 12 mm offset |
| Final drive ratio | 9:35 i = 3.8889 |
| Power transmission | Front engine and transmission (at rear) bolted together by means of a connecting tube to form a rigid drive unit. Front engine, clutch, torsionally elastic shaft (Ø 25 mm) to transmission mounted in 3 bearings, rear transmission interlocked with drive axle, twin articulated drive shafts to rear wheels |
| Transmission weight (dry) | 55 kg (121 Ibs) |
| Filling capacity | Approx. 2.5 liters multi-grade transmission oil, SAE 75 W-90, API classification GL 5 (or MIL-L21O5 B) |

Technical Data - 5-Speed Manual Transmission 016G

| Ratios 1st gear 2nd gear 3rd gear 4th gear 5th gear R.gear | 12:38 i= 3.1666 18:32 i=1.7777 23:28 i=1.2174 29:27 i = 0.9310 34:24 (35:21) i = 0.7059 (0.6000) 12:16-22:48 i= 2.9091 |
| --- | --- |
| Final drive | Helical bevel gear differential |
| Final drive ratio | 8:33 i = 4.1250 (7:33 i= 4.7143) |
| Power transmission | Front engine and transmission (at rear) bolted together by means of a connecting tube to form a rigid drive unit. Front engine, clutch, torsionally elastic shaft (Ø 25 mm) to transmission mounted in 3 bearings, rear transmission interlocked with drive axle, twin articulated drive shafts to rear wheels |
| Transmission weight (dry) | 45 kg (99 Ibs) |
| Filling capacity (specifications for USA in brackets) | Approx. 2.5 liters multi-grade transmission oil, SAE 75 W-90, API classification GL 5 (orMIL-L2105B) |

Torque Specifications - Front Axle 924/924 turbo

| Location | Thread | Tightening torque nm (ftib) |
| --- | --- | --- |
| Control arm to cross member | M12x1.5 | 65 ± 10 (48 ± 7.5) |
| Clip to control arm | M10 | 46(34) |
| Control arm to steering knuckle | M10 | 50+10 (37+ 7.5) |
| Cross member to body | M10 | 42(31) |
| Track rod to steering knuckle | M12x1.5 | 30+20(22+15) |
| Clip for stabilizer to | M8 | 13(10) |
| Body (up to Oct. 81) | M8 | 20(15) |
| Stabilizer suspension to control arm (up to Oct. 81 ) | M10 | 20 ± 5 (15 ± 4) |
| McPherson strut bearing to shock absorber strut | M14x 1.5 | 77+3(57+2) |
| Fillister head screw to clamping nut | M7 | 13+3(10+2) |
| Cover plate to steering knuckle | M7 | 10(7.5) |
| Floating caliper to steering knuckle | M12x1.5 | 85 (63) |
| McPherson strut to steering knuckle | M12x1.5 | 100 (74) |
| McPherson strut to body | M8 | 25 ± 4 (18 ± 3) |
| Spoked wheel to brake disk (LA wheel) | M14X1.5 | 130 (96) |
| Disk wheel to brake disk (st. Wheel) | M14X1.5 | 110(81) |
| Guide joint to control arm | M7 | 25(18) |
| Stabilizer suspension to body | M8 | 23(17) |
| Clip for stabilizer to suspension | M8 | 23(17) |
| Stabilizer bearing to control arm | M8 | 23(17) |

Torque Specifications - Steering 924/924 turbo

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Track rod to steering knuckle | M12X1.5 | 30+20(22+15) |
| Universal shaft to steering gear | M8 | 30+5(22+4) |
| Steering gear to cross member | M8 | 20+4(15+3) |
| Cover for pinion bearing | M6 | 7±1(5±1) |
| Cover for thrust piece bearing | M6 | 7±1(5±1) |
| Check nut for adjusting bolt | M10x1 | 25 ± 5 (18 ± 4) |
| Track rod to steering rack | M22X1.5 | 50 ± 7 (37 ± 5) |
| Track rod joint to track rod | M14X-1.5 | 30+10(22+7.5) |
| Steering wheel to steering column | M16X-1.5 | 45 ± 10 (33 ± 7.5) |
| Steering column switch to jacket tube | M8 | 15±4(11 ±3) |
| Support bearing to body | M6 | 5 (4) |
| Universal shaft to steering column | M8 | 30 ± 5 (22 ± 4) |

Torque Specifications - Rear Axle 924/924 turbo

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Bearing flange to transverse tube | M10 | 46(34) |
| Bearing flange to body | M12x1.5 | 70(52) |
| Thrust bearing to bearing flange | M10 | 46 (34) |
| Thrust bearing to body | M10 | 46(34) |
| Support bearing to body | M10 | 46(34) |
| Support bearing to strut | M8 | 23(17) |
| Axle control arm to rear axle strut | M12X1.5 | 90(66) |
| Axle control arm to rear axle strut | M12X1.5 | 103(76) |
| Axle control arm to transverse tube | M12X1.5 | 61(45) |
| Vibration damper to axle control arm and body | M12X1.5 | 61(45) |
| Universal shaft to final drive and rear wheel shaft | M8 | 42(31) |
| Adjusting lever to spring strut | M16x1.5 | 245 (180) |
| Stabilizer suspension to rear axle strut and stabilizer | M10 | 46(34) |
| Fastening clip to transverse tube | M8 | 23(17) |
| Wheel bearing cover to axle control arm | M10 | 58(43) |
| Wheel hub to rear wheel shaft | M24 x 1.5 | 380 + 70 (280 + 52) |
| Brake drum to rear wheel shaft | M24X1.5 | 350 ± 50 (258 ±37) |
| Cover plate to brake carrier | M6 | 10(7.5) |
| Floating caliper to brake carrier | M12X1.5 | 85 (63) |
| Brake line to floating caliper/ slave cylinder | M10x1 | 14(10) |
| Mounting bracket for brake line to brake carrier | M6 | 10(7.5) |
| Brake disk to wheel hub | M6 | 5.0 (4) |
| LA wheel to wheel hub | M14X-1.5 | 130 (96) |
| Steel wheel to wheel hub | M14X-1.5 | 130 (96) |
| LA wheel to brake drum | M14х1.5 | 130 (96) |
| Steel wheel (4-hole) to brake drum | M14X1.5 | 110(81) |

Technical Data - Front Axle 924

| Wheel suspension |  | Wheels independently suspended on control arms and spring struts (McPherson design) |
| --- | --- | --- |
| Springing |  | One coil spring per wheel, coaxial with spring strut |
| Shock absorbers |  | Double-acting hydraulic shock absorber struts |
| Stabilizer | Up to end model 77 Model 78 Model 79 Model 80 Model 81 some of model 82 up to end Sept. 81 In model 82 from Oct. 81 | Standard ( Optional extra ( — 20 mm — 22 mm — 23 mm — 23 mm (21 mm) (23 mm)* 21 mm 23 mm** 20mm 21.5mm |

Specifications for USA, Canada, Japan in brackets *Not as indiv. optional extra M 404 **0nly for export in conjunction with optional extra M 471

Technical Data - Front Axle 924 turbo

|  | Rest of world (USA, Canada, Japan- opt. extra) | USA, Canada, Japan- basic model(from model 81 see row) |
| --- | --- | --- |
| Wheel suspension | Wheels independently suspended on control arms and spring struts (McPherson design) |
| Springing | One coil spring per wheel, coaxial with spring strut |
| Shock absorbers | Double-acting hydraulic shock absorber struts |
|  | VW (Opt. extra Koni) | VW (Opt. extra Koni) |
| Stabilizer Ø | 23 mm USA, Canada Japanlrommod.81 21 mm (opt. extra for USA, Canada, Japan from mod. 81 23mm in conjunction with Koni shock absorber and 14 mm rear stabilizer) from mod. 82 21.5mm | 21 mm |

Technical Data - Steering 924

| Steering wheel | 2 spokes (383 mm up to end model 81 3 spokes (380 mm from model 82 Optional extra 4 spokes (362 mm 3 spokes (380 mm |
| --- | --- |
| Steering wheel ratio in the middle | 19.15:1 |
| Turning circle diameter | 10.08 m |
| Track circle diameter | 9.21 m |
| Steering wheel turns from lock to lock | 4.02 |

Technical Data - Steering 924 turbo

|  | Rest of world (USA, Canada, Japan - opt. extra) | USA, Canada, Japan - basic model (from model 81 see row) |
| --- | --- | --- |
| Steering wheel Ø | 380mm 360 mm (opt. extra) | 380mm 360 mm (opt. extra) |
| Steering wheel ratio in the middle | 22.39:1 | 19.15:1 |
| Turning circle Ø | 10.3 | 10.08 m |
| Track circle Ø | 9.5m | 9.21 m |
| Steering wheel turns from lock to lock | 4.02 | 4.02 |

Technical Data - Rear Axle 924

| Wheel suspension Springing Torsion bar Shock absorbers Stabilizer up to end model 77 from model 78 Spring strut adjustment (angle of spring strut) up to end model 77 From model 78 With (22 mm torsion bar with (23.5 mm torsion bar (for relevant models see above) | Independent wheel suspension on semi-trailing arms One round torsion bar per wheel, transverse (22mm (23.5 mm in conjunction with stabilizer (14 mm (23.5 mm from model 81 USA, Canada, Japan from chassis no. 92 АО 430199 (Sept. 79) Double-acting hydraulic shock absorbers Standard Opt. extra 018 mm Standard Opt. extra 014 mm* 23° 23°40' 19° |
| --- | --- |

* Model 80 for USA, Canada, Japan not as individual optional extra (M 404)

Model 81 and some of 82 (up to end Sept. 81 ) only export in conjunction with M471

Technical Data - Rear axle 924 turbo

|  | Rest of world (USA, Canada, Japan - opt. extra) | USA, Canada, Japan - basic model (from model 81 see row) |
| --- | --- | --- |
| Wheel suspension Springing Shock absorbers Torsion bar Ø Spacers Stabilizer Ø | Independent wheel suspension on semi-trailing arms One round torsion bar per wheel, Transverse Double-acting hydraulic shock absorbers F+S F+S (Opt. extra Koni) (Opt. extra: Koni) 23.5 mm 23.5 mm 21mm per wheel - 14mm - USA, Canada, Japan from model 81 — (Opt. Extra for USA, Canada, Japan from model 81 14 mm in conjunction with Koni shock absorbers and 23 mm front stabilizer) |

Checking Rims

Points for measuring vertical and lateral runout on outer and inner rim shoulders. Dimension "a" = 8mm

| Max. permissible vertical and lateral run-out With light alloy rims = 1.0 mm With steel rims = 1.25 mm Note It is not permitted to straighten twisted rims. |  |
| --- | --- |

Tires, Wheels, Tire Pressures

Information about permitted lire/wheel combinations is contained in the vehicle documents or Technical Information bulletins.

Tire pressures (summer and winter tires) measured with tires cold

924                924 turbo

front        2.0bar(29psi)    front        2.0bar(29psi)

rear         2.0bar(29psi)    rear         2.5bar(36psi)

Spare wheel  2.2bar(32psi)    Spare wheel  2.2bar(32psi)

924 up to model 79       Rims          Tires

Front and rear           51½Jx14       165 HR 14

from model 79            6Jx14          185/70 HR 14

924 turbo from model 79

front and rear           6Jx15          185/70 VR 1572

Wheel Alignment Adjustment Values 924/924 turbo

The following values apply to curb weight in accordance with DIN 70020 (car with full fuel tank, spare tire and tool kit)

|  | Adjustment value and tolerance | Max. difference left to right |
| --- | --- | --- |
| Front axle Toe-in (pressed with 150 N/15 kp) | +10'±5' |  |
| Track difference angle at 20' lock | -40' to -1º50' | may be affected only by replace-ment of steering arms |
| Camber | -20'±15' | 10' |
| Caster | +30’ 2°30' -15’ | 30' |
| Rear axle Toe-in per wheel | 0°±5' | 10' |
| Camber | -25'±30' (-1°±20') | 30' |
| Spring strut adjustment* (angle of spring strut) Up to end of model 77 From model 78 | 23° | 0.5° |
| With Ø 22 mm torsion bar | 23°40' | 0.5° |
| With Ø 23.5 mm torsion bar Application of Ø 23.5 mm torsion bar: in conjunction with Ø 14 mm stabilizer from model 81, all USA, Canada, Japan models from chassis no. 92А0 43 0199 (Sept. 79) | 19° | 0.5° |

| Vertical adjustment** (from model 78) Center of strut bearing (torsion bar center) under wheel center | Adjustment value and tolerance 3.5 ± 10 mm (8 ±10 mm) | Max. difference left to right 10 mm 10 mm |
| --- | --- | --- |

Specifications for USA, Canada, Japan in brackets

* 1' change in spring strut angle corresponds to approx. 6 mm change in vehicle height with ( 22 mm torsion bar 5mm change in vehicle height with ( 23.5 mm torsion bar

** For USA, Canada, Japan this figure may vary slightly. The important factor is

the bumper height. The distance from the measuring platform (level road .   surface) to top edge of bumper must be 522 ± 20 mm.

Brakes

Torque Specifications-Mechanical Brake System 924/924 turbo

| Location | Thread | Tightening torque Nm (ftib) |
| --- | --- | --- |
| Fillister head screw to damping nut | M7 | 13+3(10+2) |
| Floating caliper to steering knuckle | M12x1.5 | 85 (63) |
| Brake disk to wheel hub | M8 | 23(17) |
| Cover plate to steering knuckle | M7 | 10(7.5) |
| Wheel hub to rear wheel shaft Brake drum to rear wheel shaft | M24x1.5 M24x1.5 | 380 + 70 (280 + 52) 350 ± 50 (258 ± 37) |
| Mounting bracket for brake line to brake carrier | М6 | 10(7.5) |
| Cover plate to brake carrier | М6 | 10(7.5) |
| Brake disk to wheel hub | М6 | 5(4) |
| Floating caliper to brake carrier | M12x1.5 | 85 (63) |
| Cover plate to axle control arm | M10 | 58(43) |
| Handbrake lever to body | M8 | 21 (15) |
| Brake cable to yoke | М6 | 8.5 (6) |
| Handbrake cable to tumbuckle | М6 | 8.5 (6) |
| Brake cable bracket to brake carrier | M8 | 21 (15) |
| Wheel brake cylinder to brake carrier | M8 | 21 (15) |

Torque Specifications-Hydraulic Brake System 924/924 turbo

| Location | Thread | Tightening torque Nm (ft lb) |
| --- | --- | --- |
| Brake pressure line to tandem master brake cylinder, brake hose, distributor, wheel brake cylinder and floating caliper | M10x1 | 14(10) |
| Brake hose to floating caliper | M10x1 | 14(10) |
| Bleed screw to floating caliper | M7 | 4(3) |
| Bleed screw to wheel brake cylinder | M6 | 4(3) |
| Brake light switch to tandem master brake cylinder | M10x1 conical | 15+4(11+3) |
| Screw plug to master brake cylinder | M10xl | 14(10) |
| Tandem master brake cylinder to brake booster | M8 | 21 ( 15) |
| Brake booster to intermediate piece | M8 | 21 (15) |
| Brake booster to bulkhead | M8 | 21 (15) |
| Mounting bracket to brake carrier | M6 | 10(7.5) |

Technical Data - Brake System 924

| Designation | Remarks Dimensions | Wear limit |
| --- | --- | --- |
| Service brake (toot brake) | Hydraulic dual-circuit brake system, split up diagonally, brake booster, front wheels with sliding caliper disk brakes, rear wheels with simplex drum brakes |  |
| Handbrake (parking brake) | acting mechanically on both rear wheels |  |
| Brake disk Ø | 257mm |  |
| Effective brake disk Ø | 210mm |  |
| Brake disk thickness, new | 13mm |  |
| Min. thickness after reworking*) | 12mm | 11.5mm |
| Effective total brake lining area | 470 cm2 |  |
| Brake lining area per front wheel | 65 cm2 |  |
| Brake lining area per rear wheel | 170 cm2 |  |
| Piston Ø in brake caliper | 48 mm |  |
| Uning thickness front | 14 mm 2.0 mm |  |
| Brake drum Ø | 230mm |  |
| Min. Ø after reworking **) | 231 mm 231.5mm |  |
| Brake shoe width | 38.6mm |  |
| Brake lining thickness | 3.8...4.0 mm 2.5 mm |  |
| Brake lining thickness, oversize | 4.3...4.5 mm 2.5 mm |  |
| Piston Ø rear wheel brake cylinders | 19.05 mm |  |
| Master brake cylinder Ø up to mod. 80 from mod. 80 | 20.64 mm 23.81 mm |  |
| Brake booster up to mod. 80 from mod. 80 | 7 inches 9 inches |  |
| *The brake disk must only be reworked syrnmetrically, i.e. from both sides equally | **Use oversize brake linings |  |

Technical Data - Brake System 924 turbo/Carrera GT

| Designation | Carrera GT 924 turbo Rest of World (USA, Canada, Japan-opt. extra) Remarks | 924 turbo USA, Canada, Japan-Basic model (from mod. 81 see RoW), dimensions | Carrera GT 924 turbo Rest of World (USA, Canada, Japan-opt. extra) | 924 turbo USA, Canada Japan-Basic model (from mod. 81 see RoW) Wear limit |
| --- | --- | --- | --- | --- |
| Service brake (footbrake) | Hydraulic dual-circuit brake system with brake booster |
|  | Internally ventilated brake disks with sliding calipers front and rear. On Carrera GT additional ventilation via one airduct each side | Front wheels with sliding caliper disk brakes, rear wheels with Simplex drum brakes. |  |  |

|  | Remarks, Dimensions | Wear limit |
| --- | --- | --- |
| Brake circuit split Brake booster Ø Master brake cylinder Ø Brake disk Ø Front Rear Brake drum Ø Effective Brake disk Ø Front Rear | 924 turbo: Diagonal Carrera GT: front/rear (black/white) 9 inches Internal ratio i=3.0 924 turbo: Tandem 23.81 mm Carrera GT: Tandem stepbore 23.81/19.05 mm 282.5 mm 289.0 mm - 224.6 mm 242.0 mm | Diagonal 9 inches Internal ratio i=3.0 Tandem 23.81 mm 257.0 mm - 230 mm 210 mm - |  |
| Piston Ø in brake caliper Front Rear Piston Ø rear wheel brake cylinders Brake lining area per front wheel Brake lining area per rear wheel Total brake lining area Lining thickness Front Rear Lining thickness, oversize Brake disk thickness, new Front Rear Min. Brake disk thickness after reworking Front Rear Thickness tolerance of brake disk max. Max. Lateral runout of brake disk. Max. Lateral runout when installed Brake drum Ø new Min. Brake drum Ø after reworking Max peak-to-valley height after machining Play at brake pedal when brakes bled and engine not running | 54mm 36mm - 92cm2 63 cm2 310 cm2 13mm 13mm - 20.5 mm 20.0 mm 19.1 mm 19.2 mm 0.02 mm 0.05 mm 0.1mm - - 0.006mm min 10mm | 48mm - 19.05 mm 65 cm2 170 cm2 470 cm2 14mm 3.8...4.0 mm 4.3...4.5 mm 13mm - 12mm - 0.03 mm 0.05 mm 0.2mm 230mm - 231mm - 0.006mm min 10mm | 2mm 2mm - 18.5mm 18.6mm 231.5mm | 2 mm 2.5mm 2.5mm 11.5mm - |
| *The brake disk must only be reworked symmetrically, i.e. from both sides equally. "Use oversize brake linings Parking brake Drum brake acting mechanically on both rear wheels (handbrake) |
| Handbrake drum ( Brake shoe width Brake lining area per wheel Brake lining thickness) | 180mm 230mm 25 mm 38.6 mm 85 cm2 170 cm2 4.5 mm 3.8...4.0 mm (Oversize 4.3...4.5 mm | 181mm 231.5mm 2 mm 2.5 mm |

Technical Data - Air Conditioning from model 79

Refrigerant volume 850 g R 12 refrigerant

Refrigerating oil in compressor

230 ± 15 cm3 	Densoil 6 (up to model 78 175 cm3

or		Suniso No. 5 GS

or		Texaco Capella "E"

or		Fuchs Reniso Kes

or		refrigerating oil of identical specifications

Power consumption

Evaporator fan 160 ± 20 W

Magnetic clutch 40 W

Temperature regulation

Temperature for cut-in/cut-out of magnetic clutch, air temperature measured at evaporator outlet.

|  | Max. Cooling capacity | Min. cooling capacity |
| --- | --- | --- |
| On | 4 ± 1.5° С | 18±1.5°C |
| Off | 3±1.5°C | 15±1.5°C |

Compressor

No. of cylinders 	6

Swept volume	134 cm3  рег revolution

Weight		8.4 kg

Fusible safety plug on fluid reservoir

The safety plug fuses open at 103º С to 110° С, corresponding to an overpressure of 35 to 40 bar.

Low pressure switch on fluid reservoir The contact is open at an overpressure of under 2.2 bar

Thread sizes on the air conditioning components

| Component | Thread in inches (U Inlet | NF) Outlet | Connection for checking |
| --- | --- | --- | --- |
| Compressor Condenser Fluid reservoir Evaporator | 7/8 3/4 5/8 5/8 | 3/4 5/8 5/8 7/8 | 7/16 |

# Tightening torques

| Thread in inches | Tightening torque |
| --- | --- |
| 3/4 7/8. 5/8 | 38 Nm (28 ftib) 3 8 Nm (28 ftib) 20 Nm (15 ftib) |

Electrical System

Relays

a 	Horn relay (radiator fan from model 79)

b 	Fuel pump relay

с 	Fog lamp relay (optional extra) (air conditioning from model 79)

d 	Relay for headlamp cleaning system (optional extra)

e 	Headlamp flasher switching relay 		only B.J.L.

Warning delay relay (seat belt) 		only USA

Switch device for catalytic converter monitor 	only Japan

f 	Relay for rear window heater

g 	Combined relay for headlamp flasher and low beam (plug bridge from model 81, term. 56-56b)

h 	Relay for supplementary headlamps

i 	Relay for radiator fan (horn relay from model 79)

k 	Intermittent windshield wiper relay

I 	Turn indicator relay

Fuses from model 79

Sequence of fuses from left

| No | Consumer | Amperes |
| --- | --- | --- |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | Low beam left Low beam right Main beam left Main beam right Supplementary headlamps Brake lights, motor for concealed headlamps (hazard warning lights from model 81) Interior light Hazard warning Lamps/cigarette lighter/clock (interior-trunk-radio illumin. from model 81) Turn indicator Reversing lights, rear wiper, exterior mirrors Fresh air fan Windshield wipers License plate, trunk and Ashtray lights, rear fog lamp (instrument and switch illumination from model 81) Position lamp right Position light left, (engine cоmр. light from model 81 ) Fog lamps | 8 8 8 8 16 8 8 8 8 16 8 8 8 8 16 |

A further fuse box is located above the center electrical unit

| 1 | Ноrn | 8 |
| --- | --- | --- |
| 2 | Fuel pump (supplement. sliding air valve, warm air control, timing valve from model 81) | 16 |
| 3 | Radiator fan, el. antenna motor | 16 |
| 4 | Rear window heating | 25 |
| 5 | Condenser fan (air conditioning) | 16 |
| 6 | AC compressor, evaporator fan | 25 |
| 7 | not used (rear fog lamp from model 81) | 8 |
| 8 | El. windows | 25 |
| 9 | not used |  |

Dimensions (at curb weight in accordance with DIN) 924

Wheelbase ....................2400mm

Trackwidth, front ............1418mm

Track width, rear ............1372 mm

Length .......................4213mm

Length with USA bumpers ......4320 mm

Width ........................1685mm

Height........................1270mm

Ground clearance* ............125 mm

Turning circle................approx. 10m

Overhang angle, front* .......19.7°

rear* ........15°

924 turbo

Wheelbase ....................2400mm

Track width, front ...........1418mm

Trackwidth, rear .............1392 mm

Length........................4213mm

Length with USA bumpers ......4290mm

Width ........................1685mm

Weight .......................1270mm

Ground clearance*.............120 mm

Turning circle................approx. 10m

Overhang angle, front* .......20°

rear* ........16.4°

*at permitted gross weight

Performance Data (with DIN curb weight and half payload)

| Type Model year | 924 XK/XJ (XG/XE) 78 | 924 XK/XJ 79...85 | 924 VC 80...82 | 924 turbo 79...80 | 924 turbo 81...84 |
| --- | --- | --- | --- | --- | --- |
|  | Manual | Automatic transm | Manual | Automatic transm.. | Manual | Automalic Transm. | Manual | Manual. |
| Maximum speed | Km/h mph | 200(192) 124(119) | 195(185) 121(115) | 204 | 195 | 192 120 | 185 116 | 225 (212) 140(132) | 230 (215) 143 (134) |
| Acceleration 0...100 km/h | S | 9.9(11.5) | 11.4(13.0) | 9.6 | 11.4 | 11.2 | 13.0 | 7.8 (9.4) | 7.7 (9.3) |
| Kilometer from standing start | S | 31.0 (32-6) | 32.2 (33.6) | 30.5 | 32.2 | 32.3 | 33.6 | 28.0 (30.0) | 27.9 (29.8) |
| 1/4 mile from standing start | S | 17.4 (17.9) | 17.7 (18.4) |  |  | 17.8 | 18.4 | (16.3) | (16.2) |

Specifications for USA in brackets

Weights

| Type Model year | 924 78 | 924 79...85 | 924 80...82 | 924 turbo 79...84 | 924turbo 81. ..82 |
| --- | --- | --- | --- | --- | --- |
| Curb weight to DIN Perm. total weight Perm. axle load front* Perm. axle load rear* Perm. trailer load unbraked**/*** Perm. trailer load braked**/*** Perm. lowing weight Perm. roof load */**** Perm. drawbar load*** | row 1080 kg 1400 kg 600 kg 840 kg 500 kg 800 kg 2200 kg 75 kg 30 kg | row 1130 kg 1450 kg 650 kg 850 kg 500 kg 800 kg 2250 kg 75 kg 40 ± 10 kg | USA 1185kg/26121bs. 1500 kg/3307 Ibs. 660 kg/1455 Ibs. 880 kg/1940 Ibs. 2200 kg/4850 Ibs. 75 kg/165 Ibs. 40±10 kg/88±22 Ibs. | row 1260 kg 1550 kg 700 kg 900 kg 500 kg 1200 kg 2700 kg 75 kg .40 ± 10 kg | USA 1260 kg/2779 Ibs. 1550 kg/3418 Ibs. 700 kg/1544 Ibs. 900 kg/1985 Ibs. 75 kg/165 Ibs. |

*The perm. total weight must not, however, be exceeded.

** Up to 12% incline

*** Valid only if original Porsche spare parts are used.

**** Only if the original Porsche basic roof rack is used, otherwise only 35 kg roof load.

Caution: additional equipment (air conditioning etc. reduces payload by a corresponding amount

Filling Capacities

| Engine oil specification Engine oil volume Difference between marks on oil dipstick: Cooling system, heating Fuel tank Brake fluid reservoir Windshield washer system and head lamp cleaning system Manual transmission with differential Automatic transmission Final drive | API class SP/CC or SG multi-grade oils, see works approval Technical Information bulletins on engine oils 924 approx. 5.0 liters 924 turbo approx. 5.5 liters 924 approx. 1.2 liters 924 turbo approx. 1.6 liters Approx. 71 coolant, factory filling with anti-freeze to - 25°С Nordic countries to - 35°С 924 approx. 62 liters, of which 5 liters reserve 924 turbo approx. 84 liters, of which 9 liters reserve Approx. 0.2 liters brake fluid in accordance with SAE J 1703, DOT 3 or DOT 4 Approx. 6 liters Approx. 2.5 liters multi-grade transmission oil, SAE 75 W-90, API classification GL 5 orMIL-L2105B Filling capacity approx. 6 liters, oil change volume approx. 2.8 liters ATP Dexron II D Approx. 1 liter multi-grade transmission oil, SAE 75 W-90, API classification GL 5 orMIL-L2105B |
| --- | --- |